## Slide 1: Base Conversion
Between Powers of 2: 2, 8, 16 Examples: Rechunk
Convert each digit to binary: Lookup Table or from memory!
Merge then rechunk the bits
Convert each chunk to the appropriate digit
Base N to 10
Use Expanded Notation, or
For each digit: multiply by N, and then add the value of the digit
Base 10 to Base N
Successively divide the number by N
The concatenation of the remainders produce the final value
Consider the examples via the spreadsheet: Base Conversion

## Slide 2: Base N to Base 10
Algorithm: multiply, add, and shift
set v = 0
For each digit (from left to right)
  v = v * base; # Multiple by the base
  v = v + digit10; # Add the next digit
emit v
Consider: 16# 5a2 == 1442
16# 5a2
v: | 5 | = | 0 | * 16 + | 5 | 5
v: | 90 | = | 5 | * 16 + | 10 | a
v: | 1442 | = | 90 | * 16 + | 2 | 2
N
=
+
*

## Slide 3: Base N to Base 10
Algorithm: multiply, add, and shift
set v = 0
For each digit (from left to right)
  v = v * base; # Multiple by the base
  v = v + digit10; # Add the next digit
print v
Consider: 2# 10110101 == 181
2# 10110101
v: | 1 | = | 0 | * 2 + | 1 | 1
v: | 2 | = | 1 | * 2 + | 0 | 0
v: | 5 | = | 2 | * 2 + | 1 | 1
 | 11 | = | 5 | * 2 + | 1 | 1
 | 22 | = | 11 | * 2 + | 0 | 0
 | 45 | = | 22 | * 2 + | 1 | 1
 | 90 | = | 45 | * 2 + | 0 | 0
 | 181 | = | 90 | * 2 + | 1 | 1
N
=
+
*

## Slide 4: Base N to Base 10
Algorithm: multiply, add, and shift
set v = 0
For each digit (from left to right)
  v = v * base; # Multiple by the base
  v = v + digit10; # Add the next digit
print v
Consider: 8# == ?
8# 453
v: | 4 | = | 0 | * 8 + | 4 | 4
v: | 37 | = | 4 | * 8 + | 5 | 5
v: | 299 | = | 37 | * 8 + | 3 | 3
N
=
+
*

## Slide 5: Base Conversion of Real Numbers
Base 10 to Base N
The whole portion is divided by the new base, repeatedly
  Dividend / Divisor = (Quotient, Remainder)
  The concatenation of the Remainders provide you with the final digits
The fraction portion is multiplied by the new base, repeatedly
  Multiplier * Multiplicant = (Overflow, Product)
  The concatenation of the Overflows provide you with the final digits
Consider the examples via the spreadsheet: Base Conversion

## Slide 6: Decimal Real to Binary Real
Split the number at the radix point: whole . fractional
Put the two pieces together
With the whole part,
number = whole; while (number != 0 ){ number = number / 2; push ( number % 2 ); } pop_all();
With the fractional part
max = 10 ** stringlength(fractional); number = fractional while (number != 0 ) { number = number * 2 if ( number > max ) { emit 1 number = number - max } else { emit 0 } }

## Slide 7: Real: Decimal to Binary

## Slide 8: Example: - 39.234 Whole Part
Convert the base 10 number into base 2
Split the number at the radix point: - 39 . fractional
Put the two pieces together
number: 39 number = 39 / 2 → 19, 1 push ( 39 % 2 ) → 1 number = 19 / 2 → 9, 1 push( 19 % 2) → 1 number = 9 / 2 → 4, 1 push( 9 % 2) → 1 number = 4 /2 → 2, 0 push( 4 % 2) → 0 number = 2 / 2 → 1, 0 push ( 2 % 2 ) → 0
number = 1 / 2 → 0, 1 push ( 1 % 2 ) → 1
With the whole part,
number = whole while (number != 0 ){ number = number / 2 push ( number % 2 ) } pop_all();
100111
100111
.
-

## Slide 9: Example: - 39.234 Fractional Part
Convert the base 10 number into base 2
Split the number at the radix point: whole . 234
Put the two pieces together
max = 10 ** |234| == 1,000 number = 234 number = 234 * 2 = 0,468 number = 468 * 2 = 0,936 number = 936 * 2 = 1,872 - 1000 = 872 number = 872 * 2 = 1,744 - 1000 = 744 number = 744 * 2 = 1,488 - 1000 = 488 number = 488 * 2 = 0,976 number = 976 * 2 = 1,952 - 1000 = 952
0011101
.
With the fractional part
max = 10 ** stringlength(fractional); number = fractional while (number != 0 ) { number = number * 2 if ( number > max ) { emit 1 number = number - max } else { emit 0 } }

## Slide 10: Example: - 39.234 Both Parts
Split the number at the radix point: whole . fractional
Put the two pieces together
100111
0011101
.
With the fractional part
max = 10 ** stringlength(fractional); number = fractional while (number != 0 ) { number = number * 2 if ( number > max ) { emit 1 number = number - max } else { emit 0 } }
With the whole part,
number = whole while (number != 0 ){ number = number / 2 push ( number % 2 ) } pop_all();
-

## Slide 11: Example: 45.45 Whole Part
Split the number at the radix point: whole . fractional
Put the two pieces together
number: 45 number = 45 / 2 → 22, 1 push ( 1 ) number = 22 / 2 → 11, 0 push ( 0 ) number = 11 / 2 → 5, 1 push ( 1 ) number = 5 / 2 → 2, 1 push ( 1 ) number = 2 / 2 → 1, 0 push ( 1 ) number = 1 / 2 → 0, 1 push ( 1 ) number = 0 / 0
101101
With the whole part,
number = whole; while (number != 0 ){ number = number / 2; push ( number % 2 ); } pop_all();
101101
.

## Slide 12: Example: 45.45 Fractional Part
Split the number at the radix point: whole . 45
Put the two pieces together
max = 10 ** |45| == 100 number = 45 number = number * 2 = 90 number = number * 2 = 180 - 100 = 80 number = 80 * 2 = 160 - 100 = 60 number = 60 * 2 = 120 - 100 = 20 number = 20 * 2 = 40 number = 40 * 2 = 80 number = 80 * 2 = 160 = 100 = 60
With the fractional part
max = 10 ** stringlength(fractional); number = fractional while (number != 0 ) { number = number * 2 if ( number > max ) { emit 1 number = number - max } else { emit 0 } }
0111001
.

## Slide 13: Example: 45.45
Split the number at the radix point: whole . fractional
Put the two pieces together
With the fractional part
max = 10 ** stringlength(fractional); number = fractional while (number != 0 ) { number = number * 2 if ( number > max ) { emit 1 number = number - max } else { emit 0 } }
With the whole part,
number = whole; while (number != 0 ){ number = number / 2; push ( number % 2 ); } pop_all();
101101
0111001
.